## Slide 1: LECTURES 18-23 California’s Water
David Sedlak 03/04-14/2016

## Slide 2: Learning Goals
How did we get here?
Notes: In my two opening lectures I hope that I gave you the idea that the availability of water was a key element to the growth and development of California. During the next 5 lectures I intend to help you to understand the threats that climate change poses to California’s water system. In order to achieve that goal we need to first understand the complicated system that has developed over the past 150 years. We then need to see the weak points in the system and finally we need to start considering the options for how we will adapt in the future.

## Slide 3: Learning Goals
How did we get here?
How will climate change challenge our water systems?
Notes: In my two opening lectures I hope that I gave you the idea that the availability of water was a key element to the growth and development of California. During the next 5 lectures I intend to help you to understand the threats that climate change poses to California’s water system. In order to achieve that goal we need to first understand the complicated system that has developed over the past 150 years. We then need to see the weak points in the system and finally we need to start considering the options for how we will adapt in the future.

## Slide 4: Learning Goals
How did we get here?
How will climate change challenge our water systems?
What are our options for adaptation?
Notes: In my two opening lectures I hope that I gave you the idea that the availability of water was a key element to the growth and development of California. During the next 5 lectures I intend to help you to understand the threats that climate change poses to California’s water system. In order to achieve that goal we need to first understand the complicated system that has developed over the past 150 years. We then need to see the weak points in the system and finally we need to start considering the options for how we will adapt in the future.

## Slide 5: Wisdom of the Water Buffalo
Notes: When I first came to CA I was confused to hear people talking about water buffalos. I thought that the water buffalo (Bubalis bubalis) was native of Asia and had no known habitat in North America. But then I learned that people were talking about individuals who had taken the time and effort to steep themselves in the arcane details of CA water. After a few decades their hide becomes tough, they become grumpy and they communicate in grunts that are difficult to understand. If we want to understand how CA will deal with climate, we need to listen to the wisdom of the water buffalo. Let’s take a step back in time as in previous lectures.

## Slide 6: Wisdom of the Water Buffalo
Water flows uphill…
towards money
Notes: The wisdom of the water buffalo

## Slide 7: Wisdom of the Water Buffalo
Water flows uphill…
towards money
Except when
water rights
are involved
Notes: As we will see, water rights can keep water in applications (mainly ag) that are not that economically viable or good for the state. This causes tension and litigation

## Slide 8: Wisdom of the Water Buffalo
Water flows uphill…
towards money
Except when
water rights
are involved
Climate change is going to change everything
Notes: Keeping with our big idea, climate change may disrupt this longstanding system.

## Slide 9: Readings
http://www.ppic.org/water/
Notes: For today and Monday the PPIC lecture is probably best. Also, visit the PPIC website. For the next 3 lectures, 3 chapters from Water 4.0 will be useful.

## Slide 10: Readings
http://www.ppic.org/water/
Chapter 10: The Toilet-to-Tap Solution
Chapter 11: Turning to the Sea for Drinking Water
Chapter 12: A Different Tomorrow
Notes: For today and Monday the PPIC lecture is probably best. Also, visit the PPIC website. For the next 3 lectures, 3 chapters from Water 4.0 will be useful.

## Slide 11: Spanish/Mexican Water/Land Rights
Notes: We saw that other than damaging the native culture, the Spanish had a relatively small impact on the state. Same holds for water rights.

## Slide 12: Spanish Land Rights
Pueblo de Los Angeles
(1869)
Peralta Land Grant
Notes: The Spanish and Mexican Era did not lead to a lot of development of water because ranchers didn’t use a lot. But when CA achieved statehood under the treaty of Guadalope Hildago in 1848 that ended the war between Mexico and the US the land rights for the original settlements was accepted. For land grants for ranchos it led to large landholdings in the valley (Peralta’s didn’t stand up for long in Oakland). In LA the original Pueblo was on the LA river and it got rights to the river which is the basis for the city to have upstream rights today. (Pueblo is near downtown LA today)

## Slide 13: The Gold Rush & Water Rights
Notes: We saw that the gold rush was important to the development of the economy. It also had implications for water rights.

## Slide 14: Prior Appropriation vs Riparian Rights
Prior Appropriation: First in time/first in right (provided water is being used)
Riparian Rights: Property adjacent to water has inherent rights
California water rights have included elements of both systems.
This has been a source of controversy and disagreement.
Notes: Riparian rights generally take precedent in times of shortage. Pre-1914 and post 1914 rights important (formation of SWRCB which established permits for less than half of water). Rights to regulate all water.

## Slide 15: Hydraulic Mining and Floods
Great Flood of 1862: Atmospheric River (Pineapple Express) on top of snow caused record flooding of Sacramento Valley. Flooding was exacerbated by failure of log dams and mine tailing clogging streams.
The End of Hydraulic Mining: 1884 court case establishes hydraulic mining as a nuisance. First application of the Public Trust Doctrine.
Sacramento,1862
Notes: 1/3 of all taxable property in state lost in 1862 flood. Hydraulic mining was part of the problem. By 1884 it was terminated due to court cases in which the Public Trust Doctrine was invoked. In the interim, the Army Corp of engineers encouraged levee construction right up to the banks of the river. Sowed seeds for later delta problems. Public Trust Doctrine grew out of English Common Law in which some property rights remain with the crown (e.g., coastal access, fishing rights). Later it was applied to ecosystems (e.g., Mono Lake) as something put in trust for the benefit of the public.

## Slide 16: Early Agriculture Affects Water
Water allowed farmers to grow high value crops (not just wheat and cattle).
Water Sources:
  Riparian Access
  Groundwater
  Irrigation Districts and Federal Government
Notes: We saw that early ag was the key industry in the state after the gold rush. The thirst of ag had important impacts on the development of the state’s water system.

## Slide 17: Groundwater Basics
Aquifers are water-bearing sediments (e.g., sand)
USGS
Notes: Groundwater exists within an aquifer. Water sits in pores between the sand/silt grains. Well has screen to allow water to come in. Water table = shallow (a few feet to over 100 feet feet). Confined aquifer is recharged elsewhere due to the existence of an impermeable layer above.
Water flows downhill. Water is lost to streams and seeps at lower elevations. Can also go from stream to aquifer. Speed is typically less than cm/day. But all connected and moving. By pumping create a cone of depression and take neighbor’s water. Note: In early days mechanical pumps limited depth at which water could be taken. By turn of century gasoline and diesel pumps allowed water to be taken from over 300 feet depth. Note tradeoff between depth and energy.

## Slide 18: Groundwater Basics
Aquifers are water-bearing sediments (e.g., sand)
Pumping groundwater creates
a cone of depression
USGS
Notes: Groundwater exists within an aquifer. Water sits in pores between the sand/silt grains. Well has screen to allow water to come in. Water table = shallow (a few feet to over 100 feet feet). Confined aquifer is recharged elsewhere due to the existence of an impermeable layer above.
Water flows downhill. Water is lost to streams and seeps at lower elevations. Can also go from stream to aquifer. Speed is typically less than cm/day. But all connected and moving. By pumping create a cone of depression and take neighbor’s water. Note: In early days mechanical pumps limited depth at which water could be taken. By turn of century gasoline and diesel pumps allowed water to be taken from over 300 feet depth. Note tradeoff between depth and energy.

## Slide 19: Groundwater Overdraft
Water Level Changes since 1860
Scanlon et al. (2012)
USGS
Notes: When groundwater is over-pumped the level of the water table (or confined aquifer) decreases. This can also lead to lead to land subsidence as the land forces the pores to close. Area near Mendota CA is where maximum subsidence occurred. Why did this happen? Diesel motor and pumps revolutionized groundwater extraction and allowed farmers to go deeper. Rules didn’t really catch up.

## Slide 20: Groundwater Overdraft
Notes: Can land subsidence be reversed? No, but aquifer can be refilled and used. SCVWD as example

## Slide 21: Irrigation Districts
Imperial Valley
Notes: Merced Irrigation district is a good example of the kind of canal system that developed during this period. District funded improvements to provide irrigation water. This increased value of the land. On right is the Imperial Valley, which we discussed with the Salton Sea. Many of these water rights are appropriative but they were established before 1914 (important date).
Question: if you were a farmer who inherited land from your family how would you argue against someone taking back water rights?

## Slide 22: LA and Owens Valley
https://www.youtube.com/watch?v=UNFms_hccYE
Notes: Mulholland acquires land for LA in 1905; By 1913 water is flowing. 1930 began pumping groundwater from Owens Valley. 1927 dynamited section of Owens Valley pipeline. Water wars and eminent domain. Show Chinatown clip. Arsenic revenge?

## Slide 23: SF & Hetch Hetchy
Roosevelt & Muir
Hetch Hetchy Valley
Notes: The Hetch Hetchy va;lley was the goal of SF, but it was a bigger fight. John Muir had convinced TR to protect Yosemite Valley in 1903. He couldn’t prevail on TR to also take the neighboring Hetch Hetchy Valley or rather it took until 1913 for Wilson to allow it. 1934 water flowing into SF. Indicates impact of Federal land management on water use in CA.
http://www.acwa.com/content/climate-change/californias-water-climate-change clip on importance of snowpack.

## Slide 24: Snow: The Other Reservoir
Notes: In addition to their overall size, reservoirs rely upon extra storage capacity of snow in the adjacent landscape. For CA about 15 million acre-feet (or about as much as all of cities use) is stored in snow. Maybe you have seen the photos of the snow survey—very archaic way of managing system—DWR employees ski out and measure snow depth and moisture and use it to figure out how much snow will melt in spring. Then dams use pen-and-ink “rules curves” to determine elevation of dam during winter wet weather period. At the end of March they gradually allow the dam to refill with snowmelt.

## Slide 25: Reservoirs: Flood vs Storage
Oroville Dam Rules Curve
Notes: In addition to their overall size, reservoirs rely upon extra storage capacity of snow in the adjacent landscape. For CA about 15 million acre-feet (or about as much as all of cities use) is stored in snow. Maybe you have seen the photos of the snow survey—very archaic way of managing system—DWR employees ski out and measure snow depth and moisture and use it to figure out how much snow will melt in spring. Then dams use pen-and-ink “rules curves” to determine elevation of dam during winter wet weather period. At the end of March they gradually allow the dam to refill with snowmelt.

## Slide 26: Water for the Mega-State
Notes: LECTURE 2 starts here!
We will discuss the state’s plumbing later. We already saw the three big local projects in LA and SF. For now, it’s enough to see Hoover Dam (1928); Federal Central Valley Project (1944) and State project (1966). Greatly increased availability of water. Farmers, being rational actors switched to high water crops.

## Slide 27: Colorado River/Lake Mead
Notes: Colorado River Compact of 1922 split water between lower (CA, AZ, NV) and upper (CO, NM, UT, WY) basins. Each basin gets 293 m3/s. Lower basin about 58% CA, 37% AZ, 4% NV. Key was Boulder (later Hoover Dam) which allowed water to be stored and released. By 1940 water flowing to Imperial Valley farmers plus LA via metropolitan water district. Also generating lots of power.

## Slide 28: Water for the Mega-State
Notes: Central Valley Project (Feds).

## Slide 29: Federal Water Project (AKA Central Valley Project)
Shasta Dam
Notes: Shasta Dam was the second largest dam and linchpin of the Federal project, which sent water through Delta, allowing Feds to dam San Joaquin River. Funded and built during depression. By 1940 was delivering water. Allowed for a lot of farming in Central Valley. Most damaging project in state water system. Also provided a lot of hydro power.

## Slide 30: State Water Project
Oroville Dam
Notes: Oroville Dam was key to State Project, which barely passed legislature in 1960. Pat Brown was advocate. At time the bond was approx equal to the entire state’s budget. Provided water to Sac Valley and Bay area communities. Most water was sent south to cities (70%) and farms (30%). Completed in 1966. Largest electricity user in state because water had to be pumped over mountains.

## Slide 31: Water-Energy Nexus and SWP
Pyramid Lake: Water is released during daytime, when electricity demand is high.
Pumped back up when demand/cost is low. This process is known as pumped storage.

## Slide 32: Environmental Awareness
Notes: We discussed how the 1970s brought a change in attitude to CA. It manifest itself in two ways:

## Slide 33: Mono Lake
Notes: Mono Lake is located at the end of LA DWPs canal. It is a terminal lake (like the Great Salt Lake in Utah). All water that flows in evaporates. But when you take away its source waters, it goes out of balance. Tufa towers (limestone mainly) were exposed as lake level dropped.

## Slide 34: Mono Lake Committee
Source: Mono Lake Committee
Notes: 1975 David Gaines, MS student at Stanford gets NSF grant with students from Davis, Santa Cruz and Earlham college to study birds. Find that lake is very important and threatened by LA DWP withdrawals. Gaines and UC Davis student (later wife) Sally Judy plus David Winkler establish Mono Lake Committee. 1983 State Supreme Court uses Public Trust Doctrine to rule that state has obligation to protect Mono Lake. Finally, in 1994 LA DWP loses and has to increase lake level and decrease withdrawals. Pushes city toward alternative sources like recycling, conservation and stormwater capture.

## Slide 35: Peripheral Canal
Notes: Last stage of the canal was meant to cut through the Delta. Defeated in 1982 under governor Brown’s first term. Meant to protect water quality by avoiding mixing of pristine water with salty, high TOC water in the delta but was viewed as a water grab by Enviros, Delta farmers and farmers to the North.

## Slide 36: CA Water Today: Where
PPIC (2014)
Notes: In terms of water that falls within the state we often hear about 50/40/10 or 80/20. But that varies considerably among locations. North coast, lots of rain and few people. Sac, SJ, Tulare and CO River are key to the story. Main supplies: surface water and groundwater.

## Slide 37: Water Measurement Units
1,233 cubic meters
Notes: Sorry about acre feet! To put it into perspective, an acre foot is enough water to get about 10 people through a year. So when you hear a million acre-feet, that’s enough for about 10 million people.

## Slide 38: CA Water Today: Sources
Notes: We now have about 40 million acre-feet of water storage capacity. 15 million acre-feet is snowmelt in a typical year. If you play it right this is used as it flows in (essentially this is what you play with).

## Slide 39: CA Water Today: Sources
Notes: Compare that with the amount that is pumped (Central Valley is most important part due to ag. About 5-10 million acre feet/yr taken out but as we know it is being overdrafted. So in a typical year we get about 30-40% from groundwater and 60% mainly from surface water. In dry years more from groundwater.

## Slide 40: CA Water Today: How
PPIC (2015)
Notes: In ag about half goes to high value crops, about 1% of GDP and half goes to pastures, alfalfa, cotton, etc. Over time seeing shift to fruit and nuts. In cities about 2/3 goes to residential, about 50% indoors and 50% outdoors.

## Slide 41: CA Water Today: How
PPIC (2015)
Notes: In ag about half goes to high value crops, about 1% of GDP and half goes to pastures, alfalfa, cotton, etc. Over time seeing shift to fruit and nuts. In cities about 2/3 goes to residential, about 50% indoors and 50% outdoors.

## Slide 42: CA Water & Climate Change
Notes: Now let’s turn our attention to the potential effects that climate change will have on this system. Three main areas of concern, earlier snow melt or loss of snow. Flooding due to sea level rise and subsidence. And finally drought.

## Slide 43
Baum
Scientific American
(2015)
Notes: Droughts: How important are they and do they occur with increasing frequency under times of climate change? This figure shows the Palmer hydrologic stress index, which is a combination of soil moisture, ppt and temp. It give a sense of the severity of the current drought. Explain figure.

## Slide 44: Drought Prediction
IPCC (2013)
Notes: Let’s start by asking what we should expect under climate change. This is the RCP 4.5 scenario (midpoint). You can see that in terms of ppt or runoff, not that much change is expected. But soil moisture is expected to decrease by about 5% due to higher temperatures. But this still doesn’t quite get at what we are seeing because droughts are episodic in nature.

## Slide 45: Drought Attribution
Williams et al. (2015)
Notes: This paper that from hydrologists at Lamont Dougherty and NASA tried to get at it. They estimated that about 70% was due to variability in ppt and about 25% was due to variations in temperature. Depending which scenario or model was used, about half of this temperature increase was due to anthropogenic warming.

## Slide 46: Megadroughts & Climate Change
https://www.youtube.com/watch?v=ToY4eeWsdLc
Notes: This paper that from hydrologists at Lamont Dougherty and NASA tried to get at it. They estimated that about 70% was due to variability in ppt and about 25% was due to variations in temperature. Depending which scenario or model was used, about half of this was due to anthropogenic warming.
So the summary is that we can expect more water demand or drier conditions in general but we still don’t know enough about factors like the RRR or El Nino to say with confidence what will happen in the west.

## Slide 47: Disappearing Snowpack
CEC (2006)
Notes: Predictions also show a decrease in snowpack. Aside from recreation, what do you think are the main impacts on CA water? (1) water storage/supply; (2) hydro power (3) sensitive species.
If precipitation remains approximately constant but rain shifts to snow what does this mean for the operation of a reservoir? Getting away from old rules curves still requires prioritization among supply, flooding, environment and electricity production.

## Slide 48: The Delta Risk
Photo by Jeff Myers (baynature.org)
Notes: This is what the Delta look like today. It has undergone subsidence for a different reason than aquifers. You can see that water flows to the Clifton Court Forebay and then downstream in a manner that is far from natural, but somehow it works. Delta subsidence has occurred because peat soil was exposed to air and it oxidized (CH2O + O2  CO2 + H2O).

## Slide 49: The Delta Risk
Notes: 6.5 fault could lead to catastrophic delta island failure

## Slide 50: The Delta Risk
CA Water Education Foundation
Notes: This is an image of the Jones Tract failing on a sunny day in 2004. If the islands fail the CVP and SWP woul dbe off line for 1-3 years and it would be difficult to operate it afterwards.

## Slide 51: The WaterFix
Notes: The proposal of Delta tunnels will cost about $15 billion just to maintain the status quo. Not much of an alternative—either do it or wait for failure and reduce expeort sto SWP and CVP. The problem is that Ag cannot afford it so we would be looking at subsidizing ag.

## Slide 52: The WaterFix
Notes: LECTURE 3 STARTS HERE.
IN today’s news…price not disclosed. Estimated at $200 million.

## Slide 53: Our Big Idea: Adaptation
Well, now you’ve got
me scared.
Notes: There are a number of options facing us and no one knows the answer. Let’s examine some of the alternatives both from a technical and public policy standpoint. We will start with the technical solutions and see how they affect the policy solutions.

## Slide 54: Water System Adaptation
Technological Approaches
Water Reuse
Desalination
Managed Aquifer Recharge & Recovery
Water Efficiency Measures
Policy Approaches
Water Markets
Efficiency Mandates
Smart Growth

## Slide 55: CA Water Today: How
PPIC (2015)
Notes: In ag about half goes to high value crops, about 1% of GDP and half goes to pastures, alfalfa, cotton, etc. Over time seeing shift to fruit and nuts. In cities about 2/3 goes to residential, about 50% indoors and 50% outdoors.

## Slide 56: Water Reuse: Sewage Recycling
Notes: What are you worried about? Industrial use, too.

## Slide 57: Sewage Treatment
Activated Sludge
Notes: What are you worried about? Industrial use, too.

## Slide 58: Water Reuse: Historic Trends
Notes: The state estimates that about 0.7 is recycled of the 3-5 million acre feet per year of wastewater effluent generated in CA. Central Valley (Ag) and SoCal are leaders.

## Slide 59: Seawater Intrusion
Lenntech.com
Notes: Up until recently, the main form of reuse has been non-potable reuse. The majority is for agricultural irrigation, but the number of places where ag is close to wastewater sources is limited. In Monterrey, the regional recycling program makes a big difference (about 10% of state’s ag irrigation total). Created high value crops due to overpumping and seawater intrusion.

## Slide 60: Agricultural Reuse: Monterey Miracle
Monterey Regional Reclamation Plant
Filtration
Chlorination
Distribution
Notes: Monterey is a nice example of agricultural water reuse. Wastewater from Salinas and Moneterrey Penninsula is filtered through media and sand and chlorinated before going into purple pipes. Now they grow strawberries. Started as seawater intrusion barrier project.

## Slide 61: Urban Water Reuse (non-potable)
Indoor non-potable
landscaping
Industrial
Notes: Have you ever seen a purple pipe in your neighborhood? Historically, urban water reuse has fallen into three categories. Outdoor landscaping (most common); industril use (e.g., Chevron Refinery and EBMUD) and indoor non-potable uses (e.g., toilet flushing).

## Slide 62: The Purple Pipe Problem
Cross Connection
Notes: San Jose’s problem with South bay Recycling and cross connections in building (US, Australia, etc.).

## Slide 63: Potable Reuse: Aquifer Recharge
Trussell (2015)
Notes: Montebello Forebay near LA County since 1962. This is the groundwater recharge part of the figure.

## Slide 64: Potable Reuse: Advanced Treatment
Reverse Osmosis
Wastewater Effluent
UV/H2O2
Drinking Water
Supply
Notes: San Jose’s problem with South bay Recycling and cross connections in building (US, Australia, etc.).

## Slide 65: Reverse Osmosis
Notes: RO was invented at UCLA in 1960s, slowly developed to modern technology.

## Slide 66: UV/Hydrogen Peroxide
Notes: San Jose’s problem with South bay Recycling and cross connections in building (US, Australia, etc.).

## Slide 67: Orange County’s Reuse System
Notes: About 0.08 million acre feet-year. Operating since 1972 and recently expanded. Subjected to a lot of scrutiny (see “the toilet to tap solution”).

## Slide 68: LA Proposed Potable Reuse System
Sept. 21, 2015
MWD, Water Planning & Stewardship Committee
Notes: About 0.08 million acre feet-year. Operating since 1972 and recently expanded. Subjected to a lot of scrutiny (see “the toilet to tap solution”). 0.17 million acre feet/yr

## Slide 69: Direct Potable Reuse
Tchobanoglous (2012)
Notes: About 0.08 million acre feet-year. Operating since 1972 and recently expanded. Subjected to a lot of scrutiny (see “the toilet to tap solution”). 0.17 million acre feet/yr

## Slide 70: De Facto Water Reuse
Guo et al. (2010)
Notes: About 0.08 million acre feet-year. Operating since 1972 and recently expanded. Subjected to a lot of scrutiny (see “the toilet to tap solution”). 0.17 million acre feet/yr

## Slide 71: The Yuck Factor
https://www.youtube.com/watch?v=p-f_F3tE9rA&feature=youtu.be
Notes: Bring in bottle of new water. Discuss legitimacy.

## Slide 72: Seawater Desalination
Notes: Global Trends in desal: switch to membranes. Global capacity 12 million m3/d = 3.5 million acre feet/yr

## Slide 73: Efficiency Improvements
Example: Pressure Exchanger for energy recovery
Notes: Global Trends in desal: switch to membranes. Global capacity 12 million m3/d = 3.5 million acre feet/yr

## Slide 74: Efficiency Improvements (II)
Elimelech and Phillip (2011)
Notes: Global Trends in desal: switch to membranes. Global capacity 12 million m3/d = 3.5 million acre feet/yr

## Slide 75: Passing the Break Even Point
1
2
3
kWh/m 3
-
-
-
NRDC (2004)
Notes: Global Trends in desal: switch to membranes. Global capacity 12 million m3/d = 3.5 million acre feet/yr

## Slide 76: Passing the Break Even Point
1
2
3
kWh/m 3
-
-
-
NRDC (2004)
Notes: Global Trends in desal: switch to membranes. Global capacity 12 million m3/d = 3.5 million acre feet/yr. But he Carlksbad facility is at the bottom of the hill…

## Slide 77: Other Environmental Issues
Subsurface Intakes (aka beach wells)
Notes: Global Trends in desal: switch to membranes. Global capacity 12 million m3/d = 3.5 million acre feet/yr

## Slide 78: Other Environmental Issues
Brine Discharge
Notes: Global Trends in desal: switch to membranes. Global capacity 12 million m3/d = 3.5 million acre feet/yr

## Slide 79: Carlsbad Desalination Plant
Notes: 50 MGD plant = 0.056 Million acre feet/yr. Caost about $1 billion.

## Slide 80
Notes: LECTURE 4 starts here.
Does symbolism matter?
Water use in restaurants was 3% of SF’s water use. Only a few % of water use in restaurants goes to table water. Should we not wash dishes?
The printer paper that I put out today used 0.3 kWh of energy and emitted less than 1% of the CO2 that you would release today.
Should we put it out if it means that you might learn less?

## Slide 81
Key Points
We have the ability to capture water in wet years and store it in aquifers.
This is more challenging in urban settings than in rural areas.
It is possible to improve water efficiency in agriculture, but this will not necessarily free up water for other uses.
It is possible to reduce water use in cities, but too much conservation can have adverse consequences.
Terms
Return flows
Conjunctive Use
Consumptive/Non-Consumptive Use
Urban Heat Island Effect
Notes: LECTURE 4 starts here.
Does symbolism matter?
Water use in restaurants was 3% of SF’s water use. Only a few % of water use in restaurants goes to table water. Should we not wash dishes?
The printer paper that I put out today used 0.3 kWh of energy and emitted less than 1% of the CO2 that you would release today.
Should we put it out if it means that you might learn less?

## Slide 82: Our Big Idea: Adaptation
I feel better. But now I’m worried about the farmers.
Notes: LECTURE 4 starts here.
Last time we talked about technological solutions for adapting our water systems. We looked at how water reuse was used in agriculture, noon-potable applications and drinking water. We ended with desal and saw how it could provide water for cities. In both cases, it seemed like it might be useful to urban dwellers but it was of limited use for farmers. Today we will consider aquifer recharge and conservation. Two approaches that might make a bit more difference to ag.

## Slide 83: Desalination for Agriculture
Notes: The one thing that Paul Wolfowitz and I see eye to eye on: Israel has overdone it with respect to desal hype.

## Slide 84: Agricultural Drainage Water
Notes: While it may be impractical to desalinate seawater, desalination technology might be useful for other salt problems. One of the biggest such prpblems occurs in the SJ Valley where ag return water caused bird deformities. About 700,000 acres in San Luis Unit, which received CVP water. About 5% hooked to San Luis Canal (started in 1968). Byu 1975 stopperd over concerns w/SF Bay, drained to Kesterson where it casued bird deformities (bird embryoon left is from Kesterson)_ Desal might help farmers reuse water and avoid problem.

## Slide 85: Agricultural Drainage Water
Notes: While it may be impractical to desalinate seawater, desalination technology might be useful for other salt problems. One of the biggest such prpblems occurs in the SJ Valley where ag return water caused bird deformities. About 700,000 acres in San Luis Unit, which received CVP water. About 5% hooked to San Luis Canal (started in 1968). Byu 1975 stopperd over concerns w/SF Bay, drained to Kesterson where it casued bird deformities (bird embryoon left is from Kesterson)_ Desal might help farmers reuse water and avoid problem.

## Slide 86: Brackish Water Desalination
Notes: Brackish water coming off fields is known as return flow. This startup company is promising to solve problem—a bit dubious about economics. But let’s wait and see.

## Slide 87: Federal R&D Plans for Desal
Notes: New White House initiative: drop price by a factor of 4, from $2500/AF to $625 (starts looking like existing projects).

## Slide 88: Managed Aquifer Recharge & Recovery
Notes: Simple idea: in a wet year we put more water back into the ground. Store it in a water bank and withdraw during a dry year. This is a photo of the Kern Water Bank in the SJ Valley where a business has started in storing water because it is easy to get it into the ground.

## Slide 89: Managed Aquifer Recharge & Recovery
Notes: Simple idea: in a wet year we put more water back into the ground. Store it in a water bank and withdraw during a dry year. This is a photo of the Kern Water Bank in the SJ Valley where a business has started in storing water because it is easy to get it into the ground.

## Slide 90: Managed Aquifer Recharge & Recovery
PPIC (2012)
Notes: You can see how much water was stored before the drought got serious. Value of water can be upward of $1000/AF.

## Slide 91: Managed Aquifer Recharge & Recovery
Hansen Dam
Hansen Spreading Grounds
Notes: This is how LA captures water in the mountains and gets it into the groundwater. About 10% of cities current supply. (St. Francis Dam was one of these. Failed in 1928 and killed 431 people ending Mulholland’s career. Fictionalized in Chinatown.) You will also see recharge ponds in Santa Clara, This practice is also known as conjunctive use.

## Slide 92: Legacy Groundwater Contamination
TCE
Notes: $600-800 million treatment plant being built to cleanup groundwater in the valley because LA is losing groundwater.

## Slide 93: Stormwater Harvesting
Elmer Avenue Retrofit
(LADWP)
Before
After
Rain Gardens
Parking Lots
Notes: Public enthusiasm for stormwater harvesting at small scale due to pollution control and feeling of ownsership.

## Slide 94: Regional Recharge Facilities
Parking Lots
Atwater 2013
Notes: Realistically speaking, there are only so many places where this could be done. Need to get water into a waterbearing formation. Cannot store water within City. IN Bay Area we are mainly limited to SCV and Livermore. (Bay Margins are pretty thick clay).

## Slide 95: Stormwater Harvesting
Rory M. Shaw
Wetland Park
(Burbank, CA)
Notes: This one site is about 0.0006 million acre-feet/year. Maybe enough for 6000 people but at a cost of $50 million dollars.

## Slide 96: A Question of Scale
Notes: This one site is about 0.0006 million acre-feet/year. Maybe enough for 6000 people but at a cost of

## Slide 97: Efficiency in Agriculture
Pacific Institute (2010)

## Slide 98: Smart Irrigation Scheduling
https://www.youtube.com/watch?v=EnmhNUg0xhw

## Slide 99: Irrigation Technologies
Flood Irrigation
Sprinklers
Micro Drip

## Slide 100: Efficient Irrigation Technologies
Tindula et al. (2103)

## Slide 101: Crop Shifting
Tindula et al. (2103)

## Slide 102: Consumptive/Non-Consumptive Use
Hanak et al. (2011)
Notes: We need to differentiate consumptive from non-consuptive uses. In fact, some argue that flood irrigation is just fine b/c it recharges groundwater. Discuss ET and infiltration and ag uses where driop is used as large consumers.

## Slide 103: Personal Choices
Notes: LECTURE 5 BEGINS HERE
I want to return to the theme of differentiating between actions that feel good and actions that are effective. We cannot dispute the fact that diet affects GHG emissions. But how are you going to get your neighbor to switch? What fraction of CA population do you think can be converted by education alone? What about policies that make red meat more expensive or subsidize other diets? Or policies that otherwise make it easier. Education is a very limited tool.

## Slide 104: Urban Water Use
Cooley et al. (2007)
25
Sedlak
Notes: Per capita water use across SW US.
As we mentioned before, about 2/3 of urban use is residential and \it is generally about 50/50 indoor vs outdoor. Of course, densely populated areas, like downtown SF and Oakland essentially no outdoor residential use. This will come back under smart growth discussion, but for now accept that most of CA urban areas are single family dwelling homes with yards. Let’s start with outdoors. This figure suggests 43 as reasonable indoor value after front loading washing machines, low flow toilets, etc. Israel is around 32. I’m about 25 (Total including outdoor). So there is 10-25% reduction possible indoors. Outdoors it is even more. What is the difference between Albequerque and Las Vegas?

## Slide 105: Outdoor Water Use
Vegas
Albuquerque
Notes: Top is Nicholas Cage’s (former) mansion in Las Vegas. Bottom is Walter White’s House in Alb. Obviously the choice of landscpaing is important.

## Slide 106: Outdoor Water Use
Socovol et al. (2006)
Notes: Obviously replacing lawns saves a lot of water (up to about 80%; integrate area under curves). How do you get this to happen? Local ordinance against lawns or create incentives like “cash for grass”. Not cheap! In Las Vegas it was $60 million for 10 MGD reduction in use. Similar to what it would cost to build a water recycling plant. But once it is in you don’t have operating costs.

## Slide 107: Urban Heat Island Effect
Coutts et al. (2014)
No irrigation
irrigated
Notes: But there is a downside in terms of temperature and this is called the urban heat island effect. These are data from a study in Australia where they essentially stopped watering open parts of the city park. See difference in temperature. This is also what happens on astroturf. Evaporation is a cooling process and ET is important for keeping cool.

## Slide 108: Greening the City
Notes: Not only ET from grass but shading from trees and covering of concrete with plants makes a difference. Concrete retains a lot of heat and back-radiates at night. This is the strategy that architects use in middle east and Australia to keep cities cool. Of course, these living walls and trees require water. My guess is that we could reduce outdoor water use by 50% by concentrating on the places where it is not really needed. But there is a limit and when we go too far they city is less livable and there is more need for AC and hospitalization.

## Slide 109: Indoor Water Conservation
https://www.youtube.com/watch?v=oBMFVm5OJdM
Notes: Whether the indoor use minimum is 43, 32 or 25 it will reach a limit. We have created plumbing code requirements that will slowly drop this. But after we get to the homes that you know about could we get any lower? The 0.8 gal/flush toilet could go to 0.2 with a vacuum toilet. I think it could be a bit lower. This means front loading washing machines and low flow fixtures in every household eventually. But after that where do you look? Do you want to use a recirculating shower? Do you think that the public will be up for this?

## Slide 110: Conservation Has Its Limits
https://nextcity.org/daily/entry/water-conservation-problem-broken-sewer-pipes
Notes: But maybe we don’t want to go that far. In some places we are seeing enhanced sewer corrosion because of too much water conservation. It would be too expensive to redesign systems. Again, there is a limit to how much conservation we want to do.

## Slide 111: Graywater for Irrigation
Notes: Notwithstanding the issue of sewers, lots of individual enthusiasm for graywater from washing machine. It kind of misses the point: 75% reduction in water use going from top loader to HE front loader. How many homes can we convince to do this? More sophisticated system is harder. Only used for subsurface drip. Probably best in rural communities with septic systems.

## Slide 112
Notes: Great enthusiasm for solving problem at the building scale, especially in SF.

## Slide 113: SFPUC’s Living Machine
Notes: Living machine is a sewage treatment that treats the sewage in SFPUC’s HQ building. Used for watering plants and toilet flushing. It certainly makes people think about sewage, but it was designed more architects than engineers.

## Slide 114: Living Machine Energy & GHGs
Hendrickson et al. (2015)
Notes: We did an analysis of GHG emissions and compared it to a centralized non-potable (purple pipe) system. It was much worse for GHG and energy. And on top of that they never asked the question about waterless urinals and vacuum toilets. After all, they are not offsetting other water uses in building.

## Slide 115: Rainwater Harvesting
45,000 gal/yr * 20 yr = 2.76 acre ft
$280,000/2.76 = $100,000/acre-ft
Notes: Here is another SF project. Roofwater collection for toilet flushing. Sounds good. But $280.000 for an affordable housing building. Could the money have been better spend elsewhere?

## Slide 116: Rainwater Harvesting
Gikas and Tchobanoglous (2014)
Notes: There is merit in the idea of off-the-grid houses but probably more at the distributed scale.

## Slide 117: Water Conservation by Guilt
Notes: Let’s start with urban water conservation. One approach is to give people incentives to use less water. Social norming is an inexpensive approach where education can make a difference. Experience from WaterSmart shows that you can save a few % across an entire city just by telling people about what their neighbors do.

## Slide 118: Water Conservation by Pricing
Cooley et al. (2007)
Graduated Blocks
Notes: Another approach is by pricing. This is an example of increasing block pricing, which is the way that most CA utilities charge for water. Explain. Limitation is that even at $5 per 1000 gallons we are only talking about a bill of around $100 for a big water user. In fact, sometimes this turns out to be regressive because poor people live with lots of people in one house. Finally, in CA we have prop 218 (antitax prop) which is inconsistent with increasing block pricing.

## Slide 119: Water Conservation During Droughts
Notes: We already saw a photo of the governor visiting with the snow depth guys last summer. This figure show you what happens during droughts. LA is an instructive case study of how policy works. First, why did the water use bounce up after the drought? Revenue for water utility was part of the issue. Another thing to notice is the difference between multi-family residential and single family. A case for smart growth? Will return to city planning later.

## Slide 120: Regulating Groundwater
Notes: Agricultural water conservation is not the issue. It is the actual regulation regulation of groundwater that matters. The sustainable groundwater management act of 2014 was a first step in this process. By 2040 all gw in state will be overseen by groundwater sustainability agencies which are similar to irrigation districts—regulate basins for local benefit. Note high priority regions are in the valley because that is where overdraft is greatest. This means that farmers will need permits, etc. Note that urban groundwtaer basisn are adjudicated now.

## Slide 121: Water Markets and Trading
Notes: Letting the market take care of this is one way to go. We saw this in the water bank. You can see from this figure that water is being traded between users, but mostly it is going from ag users to urban or possibly other ag users. It’s still on the order of 0.2-0.3 mAF/yr and it seems to slowing down due to legal uncertainties. In particular water rights are an issue. If you trade water are you admitting that you don’t have a reasonable use? Also, not everywhere that wants to trade can get the water to the person who needs it. Possibly we need ISO to control the system.

## Slide 122: Water Rights, Laws & Politics
Pre-1914 Water Rights
Limitations of Public Trust Doctrine
Endangered Species Act
Political aspects of fallowing land
Giant Garter Snake
Alexander cutting the Gordian Knot
Notes: It seems like the logical think to do would be to let the people with low value water rights sell theirs to cities and high value ag. But this is a lot more complicated than you might think. If you sold a pre-1914 right it might lose value. If you try taking water rights you might have to compensate. Oh, and by the way, there are cases where endangered species have started to depend on ag water. Like the giant garter snake that lives in CA rice fields and canals.

## Slide 123: Economics and Barriers
PPIC (2011)
Notes: You can see from this figure that water is being traded between users, but mostly it is going from ag users to urban or possibly other ag users. It’s still on the order of 0.2-0.3 mAF/yr and it seems to slowing down due to legal uncertainties. In particular water rights are an issue. If you trade water are you admitting that you don’t have a reasonable use? Also, not everywhere that wants to trade can get the water to the person who needs it. Possibly we need ISO to control the system.

## Slide 124: Discussion: A Path Forward
How will cities adapt to future climate?
How will agricultural communities adapt?
What does this mean to California’s ecosystems?
How quickly do we need to act?